## Slide 1
FIRE AND SMOKE DETECTION SYSTEM
TEAM MEMBERS:
1
K R GOURINANDA
PRARTHANA R
KEERTHI PRATHAP
SIVAKRISHNA V
R SREERAG
9
40
8
53
43

## Slide 2
INTRODUCTION
Fire safety is essential in modern environments due to the widespread use of electrical devices, machinery, and flammable materials. Since fires can occur unexpectedly and spread rapidly, early detection is crucial to reduce damage and protect lives.
With the advancement of Internet of Things (IoT) technology, smart systems can monitor environmental conditions in real time and respond automatically. This project develops an IoT-based fire and smoke detection system that triggers a local alarm and sends instant alerts to the user’s mobile phone. Compared to traditional standalone detectors, this approach enables remote monitoring, faster response, and improved overall safety.
2

## Slide 3
3
TITLE
JOURNAL AND YEAR
LIMITATIONS
SOLUTIONS
Smoke Detection and Fire Safety System Using IoT
International Journal of Advance Scientific Research & Engineering Trends, Volume 5, Issue 12, April 2021
Incorrect sensor selection — MQ-7 gas sensor detects only carbon monoxide, not general smoke, causing unreliable fire detection.
Replace with MQ-2 gas sensor for broader detection of smoke and combustible gases, improving fire detection accuracy.
IoT Based Fire and Smoke Detection using Alarm and App Notification
International Journal of Innovative Research in Technology, Volume 12, Issue 8, January 2026
Overdependence on Wi-Fi — alerts fail if power, router, or network goes down during a fire.
Add SIM900A GSM/GPRS module for reliable SMS/call alerts even without Wi-Fi.
Smart Fire Detection System Using IoT
Disaster & Development, Vol. 12, Issue 02, July–December 2023
No power failure strategy — system stops working when electricity fails during a fire.
Add 18650 lithium-ion battery with IP5306 charging module to provide backup power and ensure uninterrupted safety monitoring.
LITERATURE REVIEW

## Slide 4
OBJECTIVES
4
  To design and implement a fire and smoke detection system using Arduino
  To detect smoke using MQ2 gas sensor
  To detect fire using infrared flame sensor
  To continuously monitor environmental conditions in real time
  To activate a buzzer when smoke or flame is detected
  To send SMS alert using GSM SIM900A module
  To automatically make a phone call during emergency
  To provide quick warning to prevent fire accidents
  To use separate power supply modules for reliable GSM operation

## Slide 5
BLOCK DIAGRAM & COMPONENTS
5
  Arduino Uno
  MQ2 Smoke Sensor
  Flame Sensor
  GSM SIM900A Module
  Buzzer
  IP5306 Power Bank Module (for Arduino)
  IP5306 Power Bank Module (for GSM)
  1000µF Capacitor (for GSM power stabilization)
  Lithium-ion Battery
  Connecting Wires
  Breadboard

## Slide 6
METHODOLOGY
6
The system is built using an Arduino Uno as the main controller to process data from an MQ2 Smoke Sensor and a Flame Sensor. A SIM900A GSM Module is used to send SMS and call alerts, while a buzzer provides immediate local warning. Separate power supply and a capacitor ensure stable operation. The system continuously monitors the environment and detects abnormal conditions.
  Smoke detection (MQ2)
  Flame detection (IR)
  Continuous monitoring
  Buzzer alert
  SMS & call alerts
  No repeat alerts (flag)
  Auto reset

## Slide 7
7
WORKING
  System starts and initializes all modules
  Sensors continuously monitor smoke and flame
  Arduino checks for abnormal conditions
  If detected, buzzer gives alert
  GSM module sends SMS and call
  System avoids repeated alerts using flag
  Resets after condition becomes normal

## Slide 8
CIRCUIT DIAGRAM
8

## Slide 9
  Initializes communication with GSM module
  Sets sensor pins as input and buzzer as output
  Reads flame and smoke sensor values
  Checks for fire or smoke condition
  Activates buzzer when danger is detected
  Sends alert message using GSM module
  Repeats process continuously in loop
CODE
Detailed code
9

## Slide 10
TESTING PROCEDURE
  Circuit connections verified before power ON
  Power supply and GSM module checked
  SIM inserted and network confirmed
  GSM initialization verified via serial monitor
  MQ2 Smoke Sensor tested with smoke
  Flame Sensor tested with flame
  Buzzer and GSM alerts verified for detection
  SMS and call functionality confirmed
  Alert flag checked to avoid repetition
  System reset and continuous monitoring tested
10

## Slide 11
APPLICATIONS
  Fire detection in homes and residential buildings
  Safety monitoring in offices and commercial spaces
  Industrial fire and smoke detection systems
  Laboratories and research centers
  Warehouses storing flammable materials
  Server rooms and electrical control panels
  Schools and educational institutions
  Kitchen safety monitoring systems
11

## Slide 12
CONCLUSION
The fire and smoke detection system was successfully implemented using an Arduino Uno, along with an MQ2 Smoke Sensor and a Flame Sensor for accurate detection. The SIM900A GSM Module enabled real-time SMS and call alerts, while the buzzer provided immediate local warning. The system operates continuously, offering a low-cost, reliable, and easy-to-implement solution that helps in early fire detection and reduces potential hazards.
12